# Text boxes

IR Sensor module

6.5”Wx14.3”Hx4.0”D

OPTIONAL ANALOG OUTPUTS TO BAS OR OTHER(Typ of 4)

PPM-%O2

Haloguard II/IR  Controller

10.5”Wx7.1”Hx5.7”D

3 ft. of 1/8” tubing and end of line filter provided for each IR module. Maximum extrension 200 ft. of 1/8” tubing

Locate sample point 18-24” AFF

Line Cord

120-230VAC

50/60 Hz

Cable from controller, maximum length 1000 ft.

Controller

Cable to

IR Sensor Module

OFFSCALE              POWER

HI ALARM              TEST

LO ALARM             ZERO

FAULT                MAN

RESET                 RESET

Outputs

(4) relay

contacts

Line Cord

120-230VAC   50/60Hz.

(OPTIONAL)

12V AUDIBLE ALARM

(OPTIONAL) STROBE ALARM

12VDC

8’ Cable w/ DIN Plug in Connector

(Typical for up to six (6) Sensors

IR Sensor Module, or Oxygen)

Notes:

1. 8 ft. power  cord  provided w/ wall plug connector .

2. Local  Audible /Strobe factory wired.  Remote Audible / Visual Alarms

must be 120VAC and connected to terminal in Relay Junction Box.

3. Sensor  cable is  3 conductor 18 ga. w/ foil shield.

4. Analog Outputs are adjustable  0 - 5VDC  or  0 - 10VDC.