WARNING

Analog output lines must not be connected to any kind of voltage or current source, serious damage will result.

# Text boxes

Input  +15VDC

External Power Supply

Locate sensor

18-24” AFF

8’ Cable w/ DIN plug provided

(OPTIONAL)

AUDIBLE ALARM

Maximum extension 200 FT. Use min.18 ga

3 cond.w/foil shield

Notes:

1.  Power Cord - Provided w/ wall plug adapter.

2.  Audible alarm (Optional) factory wired.  Remote Audible and Visual Alarms must be 120VAC

and connected to Alarm terminal Strip.

3.  Sensor Cable between Oxyguard( Controller and sensor - Maximum Length 200FT. Use

3 conductor 18 or 20ga. w/ foil shield.

4.  Analog Outputs (Optional) are either 0 - 5VDC, 0 - 10VDC, or 4 - 20mA.

OXYguard(

# Controller